## Slide 1: Statistical Process Control (SPC)
Nicholas Howe

## Slide 2: Agenda
What is SPC?
Introduction to SPC Charts
Examples
Diagnostics

## Slide 3: What is SPC?
To detect out of control process:
  Significant change in mean
  Significant change in variance
Examples:
  Smartphone battery life
  Particulate filtration efficiency
Quality control
  Six Sigma standards
https://www.digitaltrends.com/mobile/behind-scenes-samsung-designed-built-galaxy-s8-s8/
https://www.3m.com.sg/3M/en_SG/company-sg/all-3m-products/~/3M-Particulate-Respirator-8210-N95-160-Case/?N=5002385+3294780268&rt=rud
http://multimedia.3m.com/mws/media/312703O/masks-and-respirators-tri-fold-brochure-eng.pdf

## Slide 4: Introduction to SPC Charts

## Slide 5: Types of SPC Charts
Variable
  Continuous data
Time Weighted
  Increased sensitivity to out of control process
Attribute
  Counts data
Assumptions
Independence
Normally distributed

## Slide 6: Summary of SPC charts
Variable
𝑥 ̅,𝑠
𝑥 ̅,𝑅
Time Weighted
EWMA
𝑥, 𝑅
Tabular Cusum
𝑠^2
𝑅
𝑠
Attribute
p-chart
np-chart
c-chart
u-chart
Variable
Time Weighted
EWMA
Tabular Cusum
Attribute
p-chart
np-chart
c-chart
u-chart

## Slide 7: SPC Chart Components
2. Center
1. Upper Control Limit (UCL)
3. Lower Control Limit (LCL)
4. Observations
General Formula (L-sigma control limit)
UCL=𝜇_0+𝐿𝜎 ̂
LCL=𝜇_0−𝐿𝜎 ̂
Center=𝜇_0
General Formula (L-sigma control limit)

## Slide 8: Setting Up SPC Charts
Phase I
Get process under control or select a period where process is under control
Phase II
Use SPC chart to monitor process
Estimate required parameters from in control data
Construct SPC chart
Determine assignable cause when process signals out of control
Process in control
General Formula (L-sigma control limit)
UCL=𝜇_0+𝐿𝜎 ̂
LCL=𝜇_0−𝐿𝜎 ̂
Center=𝜇_0
General Formula (L-sigma control limit)

## Slide 9: Variable Control Charts: Chart
Individual observation chart
Parameter Estimation
Moving Range:
Chart Parameters (L-sigma control limit)
UCL=𝜇_0+𝐿𝜎 ̂=𝜇_0+𝐿∗(𝑀𝑅) ̅/1.128
LCL=𝜇_0−𝐿𝜎 ̂=𝜇_0−𝐿∗(𝑀𝑅) ̅/1.128
Center=𝜇_0
Chart Parameters (L-sigma control limit)
Note:
is the relative range statistic.
When and , then
So by

## Slide 10: Time Weighted Control Charts – EWMA
Exponentially Weighted Moving Average (EWMA)
  Better detection of small changes in mean
Parameter Estimation
EWMA Formula
𝑧_0=𝜇_0
𝑧_𝑖=𝜆𝑥_𝑖+(1−𝜆) 𝑧_(𝑖−1), 0<𝜆<1, 𝑖=1,2,…
Chart Parameters (L-sigma control limit)
UCL_i=𝜇_0+𝐿∗𝜎√(𝜆/(2−𝜆)[1−(1−𝜆)^2𝑖])
Center=𝜇_0
LCL_i=𝜇_0−𝐿∗𝜎√(𝜆/(2−𝜆)[1−(1−𝜆)^2𝑖])
EWMA Formula
Note: Typically choose

## Slide 11: Attribute Control Charts – c-chart
Useful for counts data
Suppose , then and
Parameter Estimation
Non-zero lower limit
  If , set
Chart Parameters (L-sigma control limit)
UCL=𝜇_0+𝐿𝜎 ̂=𝜇_0+𝐿∗√(𝜇_0 )
LCL=𝜇_0−𝐿𝜎 ̂=𝜇_0−𝐿∗√(𝜇_0 )
Center=𝜇_0
Chart Parameters (L-sigma control limit)

## Slide 12: Examples

## Slide 13: Individual Blood Glucose Tracking (1/2)
1. Select in-control data
Process in control
2. Check Assumptions
SPC Chart: Individual control chart
Period selected: 1989-09-01 to 1989-10-14
is set to
estimated by moving range
Ljung–Box Test: No significant autocorrelation up to lag 10
Jarque-Bera Test: Distribution is not significantly different from Gaussian

## Slide 14: Individual Blood Glucose Tracking (2/2)
3. Construct Individual Control chart
4. Construct EWMA Chart
Process first signals out of control on 1989-10-29
Process first signals out of control on 1989-10-27
EWMA detects out of control mean 2 days earlier!

## Slide 15: Singapore COVID-19 Cases (1/2)
1. Select in-control data
Process in control
2. Check Assumptions
SPC Chart: c-chart
Period selected: 2020-02-15 to 2020-03-05
is set to
is set as
Ljung–Box Test: No significant autocorrelation up to lag 10
Chi-sq Goodness of fit Test: Distribution is not significantly different from Poisson

## Slide 16: Singapore COVID-19 Cases (2/2)
3. Construct Individual Control chart
Process first signals out of control on 2020-03-06

## Slide 17: Diagnostics

## Slide 18: Violations of Assumptions
Violation of Normality
  Skewed distributions
  Heavy-tailed distributions
Violation of Independence
  Autocorrelated process
Properties of Normal Distribution
Skewness = 0
Kurtosis = 3

## Slide 19: Skewed distributions (1/3)
Can be transformed into approximately Gaussian using the Box-Cox Transformation
Box-Cox Transformation requires data to be positive
The Box–Cox transformations are defined as:
Build control charts based on transformed data
Reverse transform control limits

## Slide 20: Skewed distributions (2/3) Gamma Distribution (Right Skewed)
Histogram and QQnorm for Gamma Distribution
Histogram and QQnorm for Transformed Distribution
Box-Cox Transformation

## Slide 21: Skewed distributions (3/3) Gamma Distribution (Right Skewed)
Reverse Transform Control Limits
Box-Cox Transform
General Formula (L-sigma control limit)
UCL=𝜇_0+𝐿𝜎 ̂
LCL=𝜇_0−𝐿𝜎 ̂
Center=𝜇_0
General Formula (L-sigma control limit)

## Slide 22: Heavy-tailed distributions

## Slide 23: Autocorrelated Process: Singapore Dengue Cases (1/2)

## Slide 24: Autocorrelated Process: Singapore Dengue Cases (2/2)

## Slide 25: Thank You!